## Slide 1: MICRO CONTROLLER
MODULE 1

## Slide 2: Learning Objectives
Name some gadgets that use microcontrollers.
Define a microcontroller.
Differentiate between a computer and a microcontroller.
Describe the components of a microcontroller.
Define the pin functions of the BASIC Stamp 2 (BS 2).
Name the parts of the BASIC Stamp Board of Education (BoE).
Describe the function of each part of the BASIC Stamp BoE.
Identify and name the three main panels of the BASIC stamp Editor.
Demonstrate the function of the DEBUG command, DEBUG formatters and control characters by running simple BS2 programs.

## Slide 3: Introduction to Microcontrollers
What are microcontrollers?
Microcontrollers are special purpose computers that can do one task well.
Here we will be introduced to the BASIC Stamp 2 microcontroller developed by Parallax.

## Slide 4: Comparison
COMPUTER | MICROCONTROLLER
has the following parts: Central Processing Unit (CPU) Memory Input and Output devices | has the following parts: Central Processing Unit (CPU) Memory Input and Output devices
can run many tasks at a time | can do only one dedicated task.
Separate individual devices | can be embedded inside some other devices to control their actions.
Comparatively bigger in size | Small in size
expensive | Low cost devices
High power devices | Low power devices

## Slide 5: Microcontroller Architecture
Microcontroller is a small computer on a single IC consisting of
Central processing unit (CPU)
Memory
Input and Output ports (I/O pins)

## Slide 6
CPU:
The CPU is the “brain” that executes the programs.
it can perform addition, subtraction, division, and multiplication operations.
Memory:
The microcontroller memory is used to store programs.
It consists of cells called memory locations.
Just like a computer memory, a microcontroller has short term (volatile) memory and long term (non-volatile) memory.

## Slide 7
Input and Output Ports:
The microcontroller uses its input and output ports to communicate with the outside world.
Through its Input/Output (I/O) ports, it is possible to connect various input and output devices to the microcontroller.
Examples of input devices - switches, pushbuttons, sensors.
Examples of output devices - buzzer, LED, lamp .

## Slide 8: BASIC Stamp 2 Microcontroller
Parallax, Inc.’s BASIC Stamp 2 module has a microcontroller built onto it.
It is a black chip with lettering on it that reads “PIC16C57”.
The rest of the components on the BASIC Stamp module are also found in consumer appliances you use everyday.
Basic Stamp2 has 16 (I/O) ports.
Each one is bi-directional - this means that each I/O port can be programmed to be either an input or an output port.

## Slide 9: BASIC Stamp 2 Pin Assignment

## Slide 10: BASIC Stamp Board of Education (BoE)
To power and program the BS2 module, it needs to be integrated in a PCB board. The PCB board that comes with the BS2 is called Board of Education (BoE) .
This board is fitted with components and IC 24-pins Socket to plug in the BS2 and easily establish the following:
to connect a power supply to run the BS2.
to program the BS2 through serial or USB cable from PC.
to build electronic circuits and control them from the BS2.
to connect and control servo motors.

## Slide 11: Main parts of the BoE

## Slide 12: Function of BoE Parts
Part | Function
IC 24-pins Socket | To plug in the BS microcontroller.
Breadboard | Breadboard is a prototype board that allows insertion of components for practical tasks. The Breadboard is separated into rows of five sockets in two columns. The five sockets in each row are internally connected.
I/O Header | The vertical black 16-sockets labeled (P0P15) It is used to make connection to I/O pins of the BS2, and is referred to as the I/O Header.
Power Header | The horizontal black sockets used to supply power to the circuits .
Selector switch | Selector switch to switch ON/OFF the BoE. It has 3-positions: 0 OFF, 1 ON, and 2 Servo power ON.

## Slide 13
Part | Function
LED indicator | To indicate if the BoE is powered and switched ON.
Serial Programming Port | 9 pin connector to connect your serial cable to PC.
Battery socket | Battery socket to connect the 9V DC battery.
Servo Connections | To connect up to 4-servo motors
Reset Switch | Allows resetting of programs. Press&release to start the program on your BS2 again
5V regulator | To regulate (5.515VDC) input voltage to 5V

## Slide 14
The Power Header is divided into 3 parts as follows:
VDD  provides +5 Volts DC
VSS  represents the GND (0 Volts)
VIN Supply Voltage from battery (9V) or wall DC supply